## Slide 1: What is 3d printing

## Slide 2: 3d printinG - Origin Story
1984 – Charles “Chuck” Hull of 3D Systems develops first prototype 3D printer. He called it stereolithography and developed the STL file format widely used today.
3D printing or “rapid prototyping” is used in manufacturing to create models and prototypes quickly. Although tradition manufacturing processes, like injection molding, are cheaper per unit they are expensive and time consuming to setup (tooling) and so a quick alternative was needed.

## Slide 3: Additive manufacturing
-3D printing is an additive manufacturing process that creates 3 dimensional objects from 3 dimensional digital information.
-3 dimensional digital models are “sliced” into many 2 dimensional cross-sections that are then “printed” one on top of the other.
-There are other 3D printers that are a subtractive manufacturing process (CNC, milling) but these are usually considered a separate group and are often referred to as “machining.”

## Slide 4: 3D modeling
First you start with a 3D model:
  Modeling with 3D CAD software
  Scan an object with a 3D scanner
  Download an already made file.

## Slide 5: Slicing a 3d model with slicing software
Then 3D printing software “slices” the model into many 3D cross-sections.

## Slide 6: Slicing 3d models

## Slide 7: Sending sliced model and printing instructions to printer
Once the 3D model is sliced the data is sent to a 3D printer which recreates the object one layer at a time, stacking consecutive layers atop one another.
3D printers move along 3 axis – X,Y, and Z
  X- left to right
  Y- back and forth
  Z – up and down

## Slide 8: Representation using cut stacked cardboard

## Slide 9: Representation using cut stacked cardboard

## Slide 10: Variations of 3D Printing Technology

## Slide 11: Common Variations of 3D Printers:
SLA – Stereolithography
  UV light used to “cure” (harden) photosensitive resins or “photopolymers.”
FDM, FFF, PJP – Fused Deposition Modeling, Fused Filament Fabrication, Plastic Jet Printing
  Melted plastic filament pushed through a nozzle or “extruder.” Common plastics are ABS (acrylonitrile butadiene styrene, Legos) and PLA (polylactic acid, a bioplastic and the kind our 3D printers use)

## Slide 12: Stereolithography

## Slide 13: fdm

## Slide 14: Preparing you files for 3D Printing

## Slide 15: Preparing you files for 3D Printing
Files must be:
  STL format
Cannot have:
  Overhangs
  Intersecting Geometry

## Slide 16: Overhangs and supports
Support Material
Support material is printed to hold up geometry that overhangs. Our 3d
Overhang angle
When modeling, identify overhand angle. Use the 45° rule. Do not create geometry greater than 45°.
Failed Horizontal Overhangs
Example of failed overhangs.

## Slide 17: Intersecting Geometry