## Slide 1: Bridges

## Slide 2: History
Primitive Peoples:
  Logs
  Slabs of rocks
  Intertwined vines or ropes
Roman Empire - First Great Bridge Builders
  Timber Truss Bridges
  Masonry Arch Bridges
Europeans – Medieval Period
  Wood and stone until the rise of iron and steel use
Nineteenth Century:
  Modern Long Bridges
  Moveable Bridges

## Slide 3: Bridge Construction
Designed to:
  Carry own weight and weight of traffic
  Withstand force of high winds
Types of Bridges:
  Beam
  Arch
  Cantilever
  Suspension
  Cable-Stayed
  Truss

## Slide 4: Bridge Terms & Bridge Forces
Abutment
  Heavy supporting structures usually attached to bedrock and supporting bridge piers.
Bedrock
  Portion of Earth's mantle made of solid rock on which permanent structures can be built.
Dead load
  The force exerted by a bridge as a result of its own weight.
Dynamic load
  The force exerted on a bridge as a result of unusual environmental factors, such as earthquakes or strong gusts of wind.
Live load
  The force exerted on a bridge as a result of the traffic moving across the bridge.
Piers
  Vertical columns, usually made of reinforced concrete or some other strong material, on which bridges rest.
Suspenders
  Ropes or steel wires from which the roadway of a bridge is suspended.

## Slide 5: Bridge Forces

## Slide 6: Forces on a Bridge

## Slide 7: Dealing with Forces

## Slide 8: Beam Bridges

## Slide 9: Beam Bridges
Oldest form of bridge
Consists of a beam supported by piers at either end of the beam
Typically made from wood or metal

## Slide 10
Notes: enz_bridge.jpg

## Slide 11: Millennium Bridge, London
Notes: Millennium Bridge

## Slide 13: Arch Bridges

## Slide 14: Arch Bridges
Developed by the Romans
Traditionally made from stone or brick, but modern arch bridges are built using concrete and steel
The dead and live forces that act on the arch bridge are transmitted along the curved line of the arch into abutments or supporting structures at either end.
Arch bridges experience natural forces, which keep the bridges strong.

## Slide 15: Arch Bridges

## Slide 16: Aqueduct
Notes: aquaduct

## Slide 17: Antietam Bridge
Notes: Bridges. Stone bridge in Rock Creek Park.
Horydczak, Theodor, ca. 1890-1971, photographer.
CREATED/PUBLISHED ca. 1920-ca. 1950.
NOTES Old negative number: 220.

## Slide 18: Pont du Gard
Notes: Ancient Roman Aqueduct in southern France. Crosses the Gardon River

## Slide 19: Bridge Video!

## Slide 20: Truss Bridges

## Slide 21: Truss Bridges
A structure that consists of a number of triangles joined to each other.
Beam bridge strengthen by trusses
Lighter than ordinary beam sections of equal length
Useful for longer bridges

## Slide 22: Pratt Truss
The Pratt truss is a very common type, but has many variations. Originally designed by Thomas and Caleb Pratt in 1844, the Pratt truss successfully made the transition from wood designs to metal.
The basic identifying features are the diagonal web members which form a V-shape. The center section commonly has crossing diagonal members.

## Slide 23: Warren Truss
A Warren truss, patented by James Warren of Great Britain in 1848, can be identified by the presence of many equilateral or isosceles triangles formed by the web members which connect the top and bottom chords.

## Slide 24: Howe Truss
A Howe truss at first appears similar to a Pratt truss, but the Howe diagonal web members are inclined toward the center of the span to form A-shapes. The vertical members are in tension while the diagonal members are in compression, exactly opposite the structure of a Pratt truss. Patented in 1840 by William Howe, this design was common on early railroads.

## Slide 25: Continuous Truss Bridges
Notes: D&RG 5-span iron truss bridge #423A spanning the Grand (Colorado) River on the Montrose line at Grand Junction, Colorado / Geo. L. Beam.
Beam, George L. 1868-1935. (George Lytle),
CREATED/PUBLISHED 1912?
SUMMARY View west of an iron truss bridge crossing the Colorado River on the Denver and Rio Grande Railroad Montrose line at Grand Junction, Colorado; people and horses are on a sand bar.
NOTES Title hand-written on negative sleeve, with: "neg file no. 291," "view west," "new bridge #432.52, five 147'3 1/2" through pin-connected trusses on original stone piers and abutments, manufactured by American Bridge Co, erected on old masonry 1903-1904 by contractors McCreary & Willard," "argon - 3-4.5 s timer 1-2-3-5-6-7-8-10-11-13-15-16-18-20 on," and "print- J. L. Ozment - 9/9/1984."
Source: Jackson Thode.
Condition: negative emulsion pitted.

## Slide 26
Notes: Iowa Bridges Recording Project
MEDIUM Measured Drawing(s): 5 Photo(s): 11 Data Page(s): 14 plus cover page Photo Caption(s): 1
CALL NUMBER HAER, IOWA,31-BERN.V,1-
CREATED/PUBLISHED Documentation compiled after 1968.

## Slide 27: Cantilever Bridges

## Slide 28: Cantilever Bridges
These bridges use a diving board design technique on each side of the span
The two sides come together to support a third span
The two sides are anchored at each end by strong piers in the ground

## Slide 29: Cantilever Bridges

## Slide 30
Notes: Astoria bridge

## Slide 31: Suspension Bridges

## Slide 32: Suspension Bridges
Able to span the longest distance of any bridge type
Roadway hangs from vertical cables supported by overhead cables strung between two or more towers
Costly
Highly susceptible to winds and swaying

## Slide 33: Suspension Bridge Forces
In all suspension bridges, the roadway hangs from massive steel cables, which are draped over two towers and secured into solid concrete blocks, called anchorages, on both ends of the bridge. The cars push down on the roadway, but because the roadway is suspended, the cables transfer the load into compression in the two towers. The two towers support most of the bridge's weight.

## Slide 34: Akashi-Kaikyo Bridge, Japan
Notes: akashi_kaikyo
Today the suspension bridge reaches a free span of almost 2000m (Akashi-Kaikyo Bridge, Japan) while its cable-stayed counterpart can cross almost 1000m (Tatara Bridge, Japan, Normandie Bridge, France). Cable-supported bridges therefore play an important role in the overcoming of barriers that had split people, nations and even continents before. This cultural aspect is not less important.

## Slide 35: Brooklyn Bridge
Notes: brooklynbridge

## Slide 36: Golden Gate Bridge

## Slide 37: Bridge Video

## Slide 38
Tacoma Narrows Bridge collapsing, Tacoma, Washington, 1940
On the morning of November 7, 1940, the Tacoma Narrows Bridge twisted violently in 42-mile-per-hour winds and collapsed into the cold waters of the Puget Sound. The disaster -- which luckily took no human lives -- shook the engineering community and forever changed the way bridges were built around the world. Roadway of Tacoma Narrows Bridge twisting violently in a windstorm, Tacoma, Washington, 1940
Notes: Tacoma Narrows Bridge collapsing, Tacoma, Washington, 1940
On the morning of November 7, 1940, the Tacoma Narrows Bridge twisted violently in 42-mile-per-hour winds and collapsed into the cold waters of the Puget Sound. The disaster -- which luckily took no human lives -- shook the engineering community and forever changed the way bridges were built around the world.
Roadway of Tacoma Narrows Bridge twisting violently in a windstorm, Tacoma, Washington, 1940

## Slide 39
Notes: Tacoma Narrows Bridge collapsing, Tacoma, Washington, 1940
On the morning of November 7, 1940, the Tacoma Narrows Bridge twisted violently in 42-mile-per-hour winds and collapsed into the cold waters of the Puget Sound. The disaster -- which luckily took no human lives -- shook the engineering community and forever changed the way bridges were built around the world.
Roadway of Tacoma Narrows Bridge twisting violently in a windstorm, Tacoma, Washington, 1940

## Slide 40: Cable-Stayed Bridges

## Slide 41: Cable-Stayed Bridges
Similar to suspension bridges
Suspended by cables that run directly down to roadway from central towers
Less costly than suspension
Spans must be limited in length

## Slide 42: Sunshine Skyway Bridge, St. Petersburg and Bradenton, Florida
Notes: Sunshine Skyway Bridge
Sunshine Skyway Bridge, St. Petersburg and Bradenton, Floridahttp://www.pbs.org/wgbh/buildingbig/bridge/index.html

## Slide 43: Clark Bridge in Alton, IL

## Slide 44: Lake Pontchartrain Causeway Southern Louisiana – Nearly 24 miles long